# Hardware
## PicturePi with Projector
This variant is based on a RaspberryPi Zero and a TI DLP LightCrafter Display 2000EVM projector. A simple PCB was designed based on the Pi Projector project that can be found here: https://www.tindie.com/products/mickmake/pi-projector/
### Raspberry Pi Zero pinout:

### DLP pinout:
### GPIOs used to control the DLP
- POWER_ON:	BRCM gpio 27, pin 13 => enables DLP power thru FET
- PROJ_ON:	BRCM gpio22, pin 15 TBD: Seems not to have any effect ?
- INIT_DONE:	BRCM gpio26, pin 37
### GPIOs used to control extra HW
A light sensor BH1750 is connected to
- 3.3V:	Raspberry pin 1
- i2c SDA:	BRCM gpio23, pin 16
- i2c SCL:	BRCM gpio24, pin 18
- ADDR:	GND (slave address 0x23)
A HC SR501 motion detection sensor is connected to
- 3.3V:	Raspberry pin 1
- motion detected:	pin 22, BRCM gpio 25, wiringPi pin 6
### Picture of the adapter board
### Manually controlling the HW (outside of PicturePi):
- Enabling 5V (powers the DLP)
  gpio mode 2 out
  gpio write 2 1
- Enabling output to the projector
  sudo i2cset -y 11 0x1b 0x0c 0x00 0x00 0x00 0x13 i
  sudo i2cset -y 11 0x1b 0x0b 0x00 0x00 0x00 0x00 i
- Controlling brightness
  sudo i2cset -y 11 0x1b 0x12 0x00 0x00 0x00 <brightness R> i
  sudo i2cset -y 11 0x1b 0x13 0x00 0x00 0x00 <brightness G> i
  sudo i2cset -y 11 0x1b 0x14 0x00 0x00 0x00 <brightness B> i
  sudo i2cset -y 11 0x1b 0x3a 0x00 0x00 0x00 0x01 i
  sudo i2cset -y 11 0x1b 0x38 0x00 0x00 0x00 0xd3 i
- reading brightness
  i2cset -y 11 0x23 0x20
  i2cget -y 11 0x23 0x00 w
# Software
## Installation of Raspberry Pi OS
This document was written using Raspberry Pi OS release date 2020-08-20 (based on Debian Buster).
- Use image with desktop (most of recommended SW is not needed)
- I use balenaEtcher (https://www.balena.io/etcher) to flash the image onto the SD card
- To enable WLAN immediately on the image:
  - create an empty file ssh
  - create a file wpa_supplicant.conf in the boot partition with the following content:
    # file wpa_supplicant.conf in the boot partition
    country=DE # replace with your coutry code
    ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
    update_config=1
    network={
     ssid="wlan SSID"
     psk="password"
     key_mgmt=WPA-PSK
    }
- run sudo raspi-config and adopt defaults
  - B4: Boot into Desktop with auto-login
  - P3: Enable VNC
  - P5: Enable I2C
  - A1: Expand filesystem
- Update installed SW by
  sudo apt-get update
  sudo apt-get upgrade
- Install Java 11 JRE
  - sudo apt install openjdk-8-jdk
## Setup when using the TI DLP 2000 projector
These settings are required when using the DLP 2000 projector with the adapter board:
add the following lines to boot/config.txt:

# Add support for software i2c on gpio pins
dtoverlay=i2c-gpio,i2c_gpio_sda=23,i2c_gpio_scl=24,i2c_gpio_delay_us=2

# DPI Video Setup
dtoverlay=dpi18
overscan_left=0
overscan_right=0
overscan_top=0
overscan_bottom=0
framebuffer_width=854
framebuffer_height=480
enable_dpi_lcd=1
display_default_lcd=1
dpi_group=2
dpi_mode=87

dpi_output_format=458773
hdmi_timings=854 0 14 4 12 480 0 2 3 9 0 0 0 60 0 32000000 3
## Setup when using the HDMIPI HDMI Display
These settings are required when using the HDMIPI Display:
add the following lines to boot/config.txt:

# HDMIPI settings
hdmi_group=2 # HDMIPi for 1280 x 800
hdmi_drive=2 # for alternative modes get sound
hdmi_mode=28 # 1280 x 800 @ 60 Hz Specifcations
hdmi_ignore_edid=0xa5000080
## Installation of PicturePi
- create user and group picturepi. HOME directory gets set to /etc/picturepi to store Java preferences. Add user picturepi as sudoer
  sudo useradd -M picturepi
  sudo usermod -a -G gpio picturepi
  sudo usermod -a -G i2c picturepi
  sudo adduser picturepi sudo
- enable sudo rights without password for user picturepi
  sudo cp /etc/sudoers.d/010_pi-nopasswd /etc/sudoers.d/010_picturepi-nopasswd
  sudoedit /etc/sudoers.d/010_picturepi-nopasswd
  and change pi to picturepi
- Create directories required by PicturePi:
  sudo mkdir /opt/picturepi
  sudo mkdir /opt/picturepi/bin
  sudo mkdir /opt/picturepi/bin/libs
  sudo mkdir /etc/picturepi
  sudo mkdir /var/lib/picturepi
  sudo chown -R picturepi:picturepi /opt/picturepi
  sudo chown -R picturepi:picturepi /etc/picturepi
  sudo chown -R picturepi:picturepi /var/lib/picturepi
  sudo usermod --home /etc/picturepi picturepi
- change password for user picturepi:
  sudo passwd picturepi
- change autologin to user picturepi:
  sudo nano /etc/lightdm/lightdm.conf
  change autologin-user=picturepi
- install xscreensaver
  sudo apt install xscreensaver
- disable the screensaver and set picturepi as autostart application
  sudo mkdir /etc/picturepi/autostart
  sudo nano /etc/picturepi/autostart/picturepi.desktop

  [Desktop Entry]
  Name=PicturePi
  Comment=PicturePi
  Type=Application
  Exec=/opt/picturepi/bin/picturepi
  Terminal=false
  NoDisplay=false
- disable screensaver

  Seems enough to disable in UI config menu…?

  sudo nano /etc/xdg/lxsession/LXDE-pi/autostart
  @lxpanel --profile LXDE-pi
  @pcmanfm --desktop --profile LXDE-pi
  @point-rpi

  @xset s noblank
  @xset s off
  @xset -dpms
  @xscreensaver -no-splash
- copy PicturePi files